## Slide 1: Accelerators: TPU & FPGA

## Slide 2: In-Datacenter Performance Analysis of a Tensor Processing Unit

## Slide 3: Training vs. Inference
Typically, floating point is used for model training
  GPUs are popular for floating point matrix operations
  Throughput is the primary requirement
Inference often takes place on quantized models
  Transform floating points to integer
  Energy- and space-efficient from a hardware design perspective
  User-facing; hence, latency is king
GPUs (at least K80) are inefficient for most Google workloads

## Slide 4: Google NN Workloads

## Slide 5: Architecture
To reduce the delay of deployment, the TPU was designed to be a coprocessor on the PCIe I/O bus
The TPU instructions are sent from the host over the PCIe Gen3 x16 bus into an instruction buffer
Internal blocks are connected together by 256-byte-wide paths

## Slide 6: Compute: Matrix Multiply Unit(MMU)
Contains 256x256 MACs (Multiply Accumulate Unit)
  Performing 8-bit multiply and adds on signed or unsigned integers
    Output is 16-bit data
The matrix unit produces one 256-element partial sum per clock cycle
Can work when using a mix of 8-bit weights and 16-bit activations (or vice versa)
  Half and quarter speeds respectively

## Slide 7: IO Bandwidth
External
  14 GiB/s to PCIe interface
  30GiB/s to DDR3 interface
Internal
  10 GiB/s for control plane
  167 GiB/s for data plane

## Slide 8: Space Management
Unified Buffer is almost a third (29%) of the die
MMU is a quarter (24%)
Interfaces take up about 10%

## Slide 9: Performance
Intel Haswell
NVIDIA K80

## Slide 10: Performance: TPU
Performance is limited by memory bandwidth rather than by peak compute for most

## Slide 11: TPUv2
More memory
More bandwidth
Cluster configuration
Can do both inference and training
GPUs are catching up
  Tensor Core in V100 GPUs
  T4 for inference
Fashion-MNIST Dataset
https://medium.com/bigdatarepublic/cost-comparison-of-deep-learning-hardware-google-tpuv2-vs-nvidia-tesla-v100-3c63fe56c20f

## Slide 12: Discussion
How to design an ASIC?
  What’s the most important resource?
How to measure performance?
ASIC vs. FPGA?
  Google abandoned due to performance and power concerns

## Slide 13: Direct Universal Access: Making Data Center Resources Available to FPGA

## Slide 14: FPGA are Flexible
Computation
  Web search ranking
  Deep neural networks
  Big data analytics
Networking
  Network processing
Database/Storage
  SQL
  Key-value store

## Slide 15: Typical FPGA Deployment in Datacenters

## Slide 16: Typical FPGA Deployment in Datacenters
Problems
  Too many interfaces
  Too many namespaces
  Difficult to share
  Security issues

## Slide 17: Ideal Solution
Global names
Common communication interface
Transparent routing and resource sharing

## Slide 18: DUA Control Plane
Source: DUA NSDI’19 presentation slides
Resource management
Route calculation
Policies

## Slide 19: DUA Data Plane
Source: DUA NSDI’19 presentation slides
Overlay
  Unified interface
  Routing
Underlay
  Multiplexing
  Security

## Slide 20: How to Scale?
Hierarchies
  Naming/Addressing
  Routing
Decentralization

## Slide 21: Latency
Source: DUA NSDI’19 presentation slides

## Slide 22: Area
Altera Stratix V D5, with 172.6K ALMs of programmable logic
10% total overhead
Notes: Adaptive Logic Module (ALM)

## Slide 23: Discussion