## Slide 1: In-Datacenter Performance Analysis of a Tensor Processing Unit
Presented by Mihir Patil, Adam Stautberg

## Slide 2: Motivation
A performance analysis of Google’s TPU architecture by Google
TPU Motivation:
Cost/performance improvements in NN inference domain through domain specific hardware
Inference demands strict latency requirements because of its user focused nature
GPUs are optimized for throughput which lends to training
CPUs have none of the advantages of domain specific architecture

## Slide 3: High level idea
The TPU is single threaded and minimalistic compared to CPUs and GPUs
It has no caches, branch prediction, out of order execution, multiprocessing etc
More deterministic execution
Leverages minimalism of domain specific architecture to meet stringent application latency requirements
Maximize throughput per host interaction

## Slide 4: Details/ tech implementation / innovation
Goal is to keep the Matrix Multiply unit busy
Reading large SRAM is expensive so matrix unit uses systolic execution to reduce reads/writes of the Unified Buffer
*Throughput measured in TOPS (TeraOps/second)
Designed to plug directly into existing servers akin to GPUs
Despite having a much smaller and lower power chip, the TPU has 25 times as many MACs(Multiplier Adder Accumulator ) and 3.5 times as much on chip memory as the K80 GPU

## Slide 5: TPU block Diagram
Matrix Multiply unit does the heavy lifting
Performs 8-bit multiply and adds
16 bit products collected in 4 MiB of 32-bit accumulators
The matrix unit produces one 256 element partial sum per clock cycle
Accumulator supports double buffering
Designed for dense matrices
Matrix weights staged through on-chip Weight FIFO that reads from 8GiB off-chip DRAM
Choices determined/influenced by existing architecture/manufacturing/workloads and convenience

## Slide 6: Floorplan of TPU die
The data path is nearly two-thirds of the die
Minimal area devoted to control
Instructions are sent over PCIe following CISC tradition

## Slide 7: Five key instructions:
1. Read_Host_Memory = reads data from the CPU host memory into the Unified Buffer (UB)
2. Read_Weights - reads weights from Weight Memory into the Weight FIFO as input to the Matrix Unit.
MatrixMultiply/Convolve - Matrix Unit performs a matrix multiply or convolution from the Unified Buffer into the Accumulators. Size B*256 input, 256x256 constant weight input, giving B*256 output, taking B pipelined cycles to complete
Activate performs the nonlinear function of the artificial neuron, with options for ReLU, Sigmoid, etc. Inputs are the Accumulators, and output is the Unified Buffer.
5. Write_Host_Memory writes data from the Unified Buffer into the CPU host memory.

## Slide 8: Performance analysis/benchmarking
Adapted Roofline Performance model:
Applications are limited by either computation or memory bandwidth
Y-axis is FLOPS/sec
X-axis is FLOPS/(DRAM byte accessed) (Operational intensity)

## Slide 9: Networks and hardware used for benchmarking
Note that number of dies per server varies, so results are normalized per die

## Slide 12: Cost-Performance
Ratio of performance/watt between pairs of processors
Incremental subtracts power used by host server
* using TDP

## Slide 13: Energy proportionality under load
TPU has minimal optimizations for saving cost energy savings

## Slide 14: Related work/improvements
Performance of TPU is expected to scale 3x as memory bandwidth scales to 4x
Replacing DDR3 Weight Memory with GDDR5(used in GPUs) increases theoretical performance between 2x to 4x
Would double memory channels but allow a smaller Unified Buffer
Catapult is a contemporary but is still at least an order of magnitude slower than the TPU
Lots of room for improvement/optimization since it was developed in a 15 month timeframe
2nd Generation, and 3rd generation out, also Edge TPU
2nd Generation increases memory/bandwidth performance, 3rd is twice as fast
Not limited to 8 bit, so can be used for inference as well

## Slide 15: Questions
CISC repeat field? CISC vs RISC
Systolic execution(model parallelism?)
Decoupled access/execute

## Slide 16: Serving DNNs in Real Time at Datacenter Scale with Project Brainwave
By Adam Stautberg and Mihir Patil

## Slide 17: Motivation
Cloud service providers deploy DNN-infused applications that ingest live data streams such as search queries and videos
Computational demands of DNNs are outpacing performance growth of traditional CPUS
Specific example: Bing’s intelligent search feature
There is a clear need for low latency and high throughput
Specialized hardware can improve efficiency and performance

## Slide 18: FPGAs
FPGA – field-programmable gate array
  Parallelism targeted for a specific algorithm
  Reprogrammable
  Multiple can be allocated as a shared hardware microservice

## Slide 19: Brainwave Architecture Overview
Model parallelism and on-chip pinning
Splits DNN models into sub graphs and pins to FPGAs
This is why the hardware microservice & cloud elasticity is important

## Slide 20: Brainwave Stack Overview

## Slide 21: Tool Flow
CNNs high intensity mapped to single FGPA
Weights of bandwidth-limited RNNs pinned greedily
Unsupported or not profitable operators assigned to CPUs

## Slide 22: Brainwave NPU
Compile-time narrow precision data types
Simple, single-threaded programming model with an extensible ISA
Scalable microarchitecture that maximizes hardware efficiency at low batch sizes

## Slide 23: Narrow Precision
Proprietary ‘neural’-optimized data formats
  ms-fp8 and ms-fp9
  Mantissa trimmed to 2 or 3 bits

## Slide 24: Results

## Slide 25: Results Continued
Brainwave NPU scaled up to run on a pre-production Intel Stratix 10 280 FPGA
This engine can serve a Batch-1 high-dimensional 3,200x2,400 GRU with 480 timesteps in under 1 ms
5X that of ResNet-50 and about 25X that of AlexNet

## Slide 26: Conclusion
Key takeaway: Using configurable hardware at scale, a system can be designed without an adversarial tradeoff between latency and throughput (batching)
In Brainwave, the system and the soft NPU are co-architected in mind for each other, exploiting datacenter-scale pinning of models in on-chip memories that scale elastically beyond single-chip solutions
Narrow precision quantization is a viable approach for production DNN models. This is a large part of what allows Brainwave to compete in performance and energy efficiency without trading accuracy